## Slide 1
DDCA PROJECT
Design and Simulation of 8-Bit Signed Binary Number using the Sign-Magnitude Method
Presented by:
2620030146-Sathvika
2620030159-Kaushal
2620030167-Sasidhar
2620030171- Renu Sree

## Slide 2
8-Bit Signed Binary Representation
Design and simulation using the sign-magnitude method
SIGN
1 BIT
Most significant bit — determines polarity
MAGNITUDE
7 BITS
Absolute value stored as ordinary binary
SIMULATION
Logisim
Live demonstration of field isolation

## Slide 3
Problem Definition
What must the design accomplish?
1
Allocate the Fields
Reserve 1 bit for sign and 7 bits for magnitude.
2
Define Valid Values
State the range and handle the duplicate encodings of zero. The representation must separate sign from absolute magnitude and be directly verifiable in Logisim.
3
Demonstrate Behavior
Use Logisim to expose the sign and magnitude branches.

## Slide 4
Design & Methodology
One sign bit, seven magnitude bits — Value = (−1)^S × M, with S ∈ {0,1} and M stored as ordinary 7-bit binary.
SIGN · 1 BIT
S = 0 → Positive
S = 1 → Negative
MAGNITUDE · 7 BITS
M₆ M₅ M₄ M₃ M₂ M₁ M₀
Range: 0 to 127
Range
Numerical range: −127 to +127
Dual Zero
+0 = 00000000 and −0 = 10000000
Encoding Examples
Value
8-Bit Code
+45
00101101
−45
10101101
+127
01111111
+0
00000000
−0
10000000

## Slide 5
Logisim Design
Route the word, then inspect the fields
Place Input Pin
Add 8-bit INPUT pin labeled INPUT.
Configure Splitter
Set bit width 8 and fan-out 2.
Attach Probes
Probe SIGN (1) and MAGNITUDE (7).
Verify MSB Routing
Ensure bit 7 reaches sign output.
Signal Flow
INPUT → SPLITTER → SIGN and MAGNITUDE
Input Pin
8 data bits, labeled INPUT
Splitter
Bit width = 8, fan-out = 2. Does not alter the code.
Probes
1-bit sign output + 7-bit magnitude output
Optional Display
Raw word verification probe

## Slide 6
Logisim Implementation
Circuit Breakdown
Signal processing system showing binary input (0101101, representing +45) passing through a splitter that divides the signal into SIGN and MAGNITUDE outputs.
Input
8-bit word enters the circuit at the input pin
Splitter
Bit 7 routed to SIGN; bits 6–0 routed to MAGNITUDE
Output
Two probes display isolated fields in real time

## Slide 7
Simulation Results
Demo: Positive and Negative 45
Input
SIGN
MAGNITUDE
Result
00101101
0
0101101
+45
10101101
1
0101101
−45
00000000
0
0000000
+0
10000000
1
0000000
−0
Toggling the MSB (Sign Bit) flips the sign of the number while the 7-bit magnitude field remains identical — confirming the splitter correctly isolates the fields.

## Slide 8
Conclusion & Key Takeaways
Our project successfully explored the 8-bit signed binary representation, demonstrating its design principles and practical application.
1
Sign-Magnitude Clarity
The sign-magnitude method provides a straightforward way to represent signed numbers, clearly separating polarity from the absolute value.
2
Logisim Validation
Our Logisim simulation effectively verified the isolation of sign and magnitude fields, confirming the design's integrity.
3
Digital Logic Foundation
Understanding binary representations like sign-magnitude is fundamental for developing and debugging digital logic circuits and systems.